## Slide 1: HERMES Technology Readiness Levels
Nasa rasc-al
Mario Saenz
College of Engineering
NASA RASC-AL project

## Slide 2: What is the TRL scale?
It is NASA’s measure of technology maturity
It is split into 9 levels, each describing a different stage from idea to fully proven and tested

## Slide 3: The 9 TRL levels
TRL | Definition | Environment
1 | Basic principles observed | 
2 | Concept formulated | 
3 | Proof-of-concept | Analytical/lab
4 | Component validated | Lab
5 | Component validated | Relevant
6 | Prototype demonstrated | Operational
7 | System prototype | Space
8 | Flight-qualified | Space
9 | Flight-proven | Mission

## Slide 4: Level required for our application
New critical technologies must reach TRL level 6 by Preliminary Design Review
Why?
Demonstrated as an integrated prototype
Tested under mission-relevant conditions
Reduced risk of late changes or cost increases

## Slide 5: Differences between TRL 4, 5, and 6
TRL 4 – Lab validation
Components/breadboards tested in lab
Early prototypes, low fidelity
TRL 5 – Relevant environment validation
Components tested in an environment that approximates key mission conditions
Higher fidelity tests
TRL 6 – Prototype demonstration in relevant environment
Integrated system/subsystem (not just components)
End-to-end prototype operating under mission-like conditions
Reliable performance demonstration across scenarios, including error cases

## Slide 6: What testing is needed to advance in the TRL scale
TRL 4 -> 5
Test components in relevant environments (balloon flight, LoRa outdoor)
TRL 5 -> 6
Demonstrate an integrated HERMES prototype under realistic conditions (full system, e.g. balloon, power, antenna, etc)
Mars analog environments
Full end-to-end data flow
TRL 7-9
Demonstration in space environments

## Slide 7: What space qualified means
Environmental qualification
Vibration and shock
Thermal vacuum cycling
Radiation testing
Parts and process control
NASA-approved EEE parts
Environmental stress testing, lot screening
Documentation and test reporting
Design files
Qualification test reports